02 November 2006

Added macro text 01 Sept 2010

Modified macro text 20 March 2018

COMPASS for Pressure, DUT SETUP

CRYSTAL MODEL 33 and IS33

Three DUT setups and two macros are provided with COMPASS:

- Crystal 33, Hi / Lo Sensors,	Advanced DUT, Requires Enhanced COMPASS

- Crystal 33, Hi Sensor,		Simple DUT, Compatible with Basic COMPASS

- Crystal 33, Lo Sensor,		Simple DUT, Compatible with Basic COMPASS

- ParseCrystal33Lo

- ParseCrystal33Hi

- ExtractText (globalCode macro)

For COMPASS Enhanced users, the Advanced DUT setup combines outputs for both the high and low pressure sensors.  For COMPASS Basic users, two separate simple DUT setups are provided.

CRYSTAL 33, ADVANCED DUT SETUP SUMMARY:  Use this setup for COMPASS Enhanced.

The RS232 port settings are hard coded to 4800,N,8,1.  Handshaking must be set to Xon/Xoff which enables power to the port on pins 4 and 7.  There is no Command Terminator and the Response Terminator is set to “>” – the “100” is a field length delimiter.

Create two outputs:

Setup the outputs…

Edit the commands…

Repeat process for the Lo Pressure sensor, but use the ParseCrystal33Lo macro.

<End Advanced DUT setup>

CRYSTAL 33, SIMPLE DUT SETUP SUMMARY: Use this setup for COMPASS Basic users.

Next, configure the Output tab:

Next, configure the Communications Tab which include the Edit Commands button:

Edit Commands…

Repeat process for the Lo Pressure sensor, but use the ParseCrystal33Lo macro.

<End DUT setup>

Macros:

- ParseCrystal33Lo

- ParseCrystal33Hi

- ExtractText (globalCode macro)

- ParseCrystal33Lo (replyParser macro)

Function ParseCrystal33Lo(Reply, ParamID, cRange)

p = instr(Reply, "P1")

If P <=0 Then Exit Function

cDebug.LogStatus  "Lo Reply P:" & p & "===" &  Mid(reply,p+2,1) & vbcrlf & reply

If Mid(reply,p+2,1) = "T" Then Exit Function

temp = Mid(reply,p)

Prs = qextract(temp,2,4,",")

If Prs = "" Or instr(prs,",") = 0 Then Exit Function

Prs = qextract(Prs,0,1,",")

cDebug.LogStatus "Lo Prs= " & Prs

ParseCrystal33Lo = Prs

End Function

2. ParseCrystal33Hi (replyParser macro)

Function ParseCrystal33Hi(Reply, ParamID, cRange)

p = instr(Reply, "P2")

If P <=0 Then Exit Function

cDebug.LogStatus  "HI Reply P:" & p & "===" &  Mid(reply,p+2,1) & vbcrlf & Reply

If Mid(reply,p+2,1) = "T" Then Exit Function

temp = Mid(reply,p)

Prs = qextract(temp,2,4,",")

If Prs = "" Or instr(prs,",") = 0 Then Exit Function

Prs = qextract(Prs,0,1,",")

cDebug.LogStatus "Hi Prs= " & Prs

ParseCrystal33Hi = Prs

End Function

3.  ExtractText (globalCode macro), should already be in COMPASS

'--------------------------------------------------------------------

'

'This function accepts an initial string, start position, end postition

'and a separator and returns the parsed value.

'Teststring$ => The string to pull apart

'StartSeparator%=> # of the separator to start copying from

'EndSeparator => # of the separator to stop copying to

'Separator$ => String used to separate areas of the text

'

'The function returns null if the the value is invalid

'

'--------------------------------------------------------------------

Public Function qextract(teststring, Startseparator, EndSeparator, Separator)

Dim count1

Dim newstring

Dim allData

Dim i

Dim Max

If teststring = "" Then Exit Function

allData = Split(teststring, Separator)

count1 = UBound(allData)

If count1 < Startseparator Then Exit Function  'Must have the value in it before leaving

If (EndSeparator - 1) > count1 Then

Max = Count1

Else

Max =  EndSeparator - 1

End If

newstring = ""

If Startseparator > Max Then

'newstring = allData(Startseparator)

For i = Startseparator To count1

newstring = newstring & allData(i)

If i <> count1 Then

newstring = newstring & Separator

End If

Next

Else

For i = Startseparator To Max

newstring = newstring & allData(i)

If i <> Max  Then

newstring = newstring & Separator

End If

Next

End If

qextract =  Trim(newstring)

End Function